INSTRUCTIONS FOR USE (IFU)

Product Name: Bougie Introducer Ranges

SINGLE USE – This product is designed as a Single Use product.

WARNINGS:

1. Single Use Only

2. Sterile if package is unopened, undamaged and within shelf life date

3. Do not re-sterilise.

4. Do not expose to temperatures above 49°C.

5. This product must be pre-use checked prior to use.

6 The product must not be used for nasal intubation.

PRE-USE CHECKS: DO NOT use this product unless these checks are fully satisfactory.

1. If applicable, check product is within its specified sterile shelf life

2. Visually check whole device for completeness, discolouration, damage and flaws.

INSTRUCTIONS FOR USE: These directions are general guidelines intended for use by qualified medical personnel. Any Instructions and contraindications given are not exhaustive and it is the clinician’s responsibility to ensure the safe, correct use of this product. The Bougie is designed to give good directional control during routine or difficult oral intubations when the laryngeal inlet cannot be completely seen.

1. Select the correct size and type of Bougie and place the lubricated Bougie in the pharynx and manipulate into an appropriate position to enter the larynx and into the trachea.

2. Thread the lubricated ET Tube over the Bougie.

3. Slide the ET Tube through the larynx and into the trachea.

4. Hold ET Tube in place and gently withdraw the Bougie.

5. Follow instructions provided with ET Tube to complete safe intubation.

6 Once the Bougie has been withdrawn from the patient it must be discarded and not   reintroduced at a later stage in the procedure.

Storage:  Store product inside containers or outer boxes in a clean, dry area.

Storage should be within a Temperature range of 10 – 30⁰C.

Do not expose to direct sun light or UV light.

Manufactured by:

Distributed by: